## Slide 1: Towards Stability Analysis of Data Transport Mechanisms: a Fluid Model and an Application
Gayane Vardoyan*, C. V. Hollot†, Don Towsley*
*College of Information and Computer Sciences,
†Department of Electrical and Computer Engineering

## Slide 2: Background
Stability well-understood: TCP Reno, STCP.
Less so: CUBIC, H-TCP.
  Reason: lack of a suitable modeling framework.
Notes: There are many different variants of TCP, and some of them are well-understood in the context of stability. Examples are TCP Reno and Scalable TCP. Their response functions (how they increase and decrease cong. window) are relatively simple. However, some variants exhibit more complex behaviors when increasing or decreasing. The exact dynamics of how these variants interact with the network are not fully understood, partly due to a lack of a suitable modeling framework within which they can be analyzed. Examples are CUBIC and H-TCP.

## Slide 3: Contributions of this Work
New modeling framework applicable to wide variety of loss-based protocols.
Application to TCP CUBIC.
  Result: CUBIC is locally asymptotically stable.
Simulation framework to test and validate the models.
Notes: To address this problem, we make the following contributions.
Loss based protocols are protocols that utilize loss information to make decisions about increasing cwnd or sending rate, or backing off upon congestion detection.
These are schemes that include not only ACK-based algorithms, but also packet marking schemes as in ECN (Explicit Congestion Notification).
CUBIC result is previously unknown.

## Slide 4: Brief Introduction to Stability
unstable equilibrium
global
stable equilibrium
two local
stable equilibria and one unstable equilibrium
Notes: To get an intuition on certain concepts of stability theory, it helps to begin by looking at a simple physical system.
Intuitively, in an unstable system, small disturbances to system can cause large changes in the response.

## Slide 5: Stability: Difference in Responses
x(t)
time
stable, monotonic response with convergence
Notes: Suppose that we track some variable, x. It could be distance or position, for example.
Shown in this plot is a monotonically stable response (e.g. exponential decay).

## Slide 6: Stability: Difference in Responses
x(t)
time
stable, oscillatory response with convergence

## Slide 7: Stability: Difference in Responses
x(t)
time
oscillatory response without convergence
Notes: Oscillatory unstable response.

## Slide 8: Stability: Difference in Responses
Undamped oscillation is undesirable behavior.
Convergence to a fixed point is desirable behavior.
Notes: The blue curves represent desirable responses in the context of congestion control. The red is not a desirable response because there is no convergence to a fixed point.
In the context of nonlinear dynamics, the red curve is considered stable (for example, it could be a limit cycle), but in the context of data transport mechanisms, we consider it unstable behavior.

## Slide 9: Instability with TCP CUBIC
This choice of
initial conditions leads to unstable behavior.
Fluid model simulation.
Link capacity of
1 Gbps,
delay of 100 ms.
Notes: This plot was created using our fluid model to be discussed further in the talk. Red line: fixed point value. Blue curve: trajectory from the fluid model.
In general, large delays tend to have destabilizing effects on systems. However, in some cases, the system can be stabilized with the right choice of initial conditions.
In such cases, knowing the dynamic properties of the system can be imperative to its proper and effective operation, because a stability analysis can yield the conditions for the system’s stability.

## Slide 10: Stability with TCP CUBIC
Fluid model simulation.
Link capacity of
1 Gbps,
delay of 100 ms.
This choice of initial conditions leads to stable behavior.

## Slide 11: The Lesson
TCP CUBIC can be ill-behaved.
In general, more deviation from fixed-point  more instability.
Impact on performance metrics
like bandwidth utilization.
Effective modeling  conditions for stability
 ensure efficient operation of the protocol.
Notes: Simulations show that there exist ranges of parameters where TCP CUBIC is ill-behaved. In general, the more we deviate from the fixed-point value of cwnd or sending rate, the more unstable the system behaves. This in turn has an impact on performance metrics like bandwidth utilization. Hence, effective modeling techniques can yield conditions for stability and ensure efficient operation of the protocol.

## Slide 12: Previous Work
Misra et al. “Fluid-based Analysis of a Network of AQM Routers Supporting TCP Flows with an Application to RED.” ACM SIGCOMM 2000.
Hollot et al. “A Control Theoretic Analysis of RED.” INFOCOM 2001.
  Analyze system above, present design guidelines for stable AQM operation.
Liu et al. “Fluid Models and Solutions for Large-Scale IP Networks.” ACM/SigMetrics 2003.
  Uses (*) as a starting point. Model a network of AQM routers. Obtain transient behavior of average queue lengths, packet loss probabilities, latencies.
Notes: There are lots of examples in literature of using fluid models and differential equations to model the dynamics of TCP.
Perhaps the most notable is the paper by Misra et al...One of the main contributions is a fluid model that describes the average cwnd of Reno.W(t) is the average congestion window, tau is delay, and lambda(t) is loss rate. There are many other examples of using fluid models to describe behavior of TCP and other data transport protocols. But all of these papers present simulation results and demonstrate that the models are quite accurate. So these modeling techniques are very powerful not only in the number and types of system parameters they can describe, but also in being able to model how real systems actually work.

## Slide 13: Definitions
Term | Definition
 | per-flow capacity
 | link delay
 | the size of the cwnd immediately before loss
 | the time elapsed since last loss
 | the cwnd as a function of time
 | a loss probability function
 | fixed-point value of

## Slide 14: TCP CUBIC: Definition
Congestion window function is given by
- scaling factor,
- multiplicative decrease constant,
- elapsed time since last loss,
- size of cwnd immediately before last loss.

## Slide 15: TCP CUBIC in Steady State
Notes: Here is how CUBIC’s cwnd evolution looks as a function of time, in stable state.

## Slide 16: Modeling CUBIC
Reno: AIMD
Scalable TCP: MIMD
CUBIC:
Notes: CUBIC is defined explicitly in terms of Wmax and s, which in tern are both dependent on time. Hence, we cannot apply previous modeling techniques to this protocol. Moreover, note that congestion controllers can be generated or engineered in ways that don’t lend themselves to traditional modeling techniques. Conclusion: previous models are not always adequate for modeling CC algos with complex rules.

## Slide 17: New Approach
Observation: loss-based protocols have in common:
  max cwnd before loss, Wmax(t)
  time since last loss, s(t)
Derive DEs for
  instead of for W(t)!
Notes: Hence, we have to adapt a new approach. We first make the following key observation: all loss-based algo have in common two variables: Wmax, and s(t). These variables, in turn can be used to completely define a cwnd or sending rate function. Hence, a natural approach is to derive...

## Slide 18: Example: TCP CUBIC
Notes: Instead of modeling the red curve (cwnd), we instead want to model the blue and green curves. As you can see, the max. cwnd remains constant until the next loss occurs. The time between losses grows linearly with time during a congestion epoch, and resets to zero upon loss. We can apply this methodology to any loss-based congestion controller. For example, TCP Reno.

## Slide 19: Example: TCP Reno

## Slide 20: New Model
System of differential equations
Loss probability function
Notes: Note: W(t) needs to be either explicitly given or derived.
We point out that this framework is not dependent on any specific W(t) function. That is, in order to apply the framework, one only need to derive or define W(t) and then substitute it into these DEs. Hence, this framework provides not only opportunities to analyze existing protocols, but also an easy way to design and analyze the stability of new ones.
This loss prob. function is an approximation of the M/M/1/B drop probability when the buffer size B tends to infinity. It is sometimes used in fluid flow approximation models, and we chose this function because of its simplicity.

## Slide 21: New Model: First DE
packet loss rate
change in maximum congestion window size
delayed by one round trip time, since loss occurs at a congestion point, not at the source

## Slide 22: New Model: Second DE
packet loss rate
time since last loss grows by one time unit,
and is reset to zero upon new loss
delayed by one round trip time, since loss occurs at a congestion point, not at the source

## Slide 23: Application to CUBIC
System of differential equations
Loss probability function
Congestion
window
function

## Slide 24: Asymptotic Stability
Lyapunov stability
convergence to fixed point
trajectory

## Slide 25: Examples: Fluid Model
initial conditions deviate too far from fixed point
initial conditions yield asymptotically stable response
Notes: These simulation examples demonstrate how CUBIC can go from stable operation to unstable via a change in initial conditions.

## Slide 26: Model Validation
NHPL – Non-Homogeneous
Poisson Loss Simulation
Possible application of what we learned: fixed point value can be used to choose initial ssthresh.
Notes: NHPL treats inter-loss time as a non-homog. Poisson process.
Possible application of what we’ve learned: more intelligent ssthresh choices.

## Slide 27: Summary
New modeling framework consisting of a set of differential equations, loss probability function, and congestion window or sending rate function.
Model used to analyze TCP CUBIC and establish that it is locally asymptotically stable.
New lightweight simulation framework generalizable to a variety of protocols.
  Used this to validate the fluid model.
  See Vardoyan et al. arXiv:1801.02741, Jan 2018 for full proofs, convergence result, detailed description of simulation framework, and more...

## Slide 28: Thank you!
Questions?

## Slide 29: Model Equivalence

## Slide 30: Initial Attempt to Model CUBIC
CUBIC has a fixed point located at its saddle point.
Derive DE for cwnd, W(t).
Linearize DE about fixed point.
Obtain dW(t)/dt=0.
W(t)
Notes: What makes CUBIC not amenable to analysis within the previous framework is that CUBIC has a fixed-point value located at the saddle point of the cubic function, as shown here.
Hence, a linearization of a DE for W(t) about the fixed point would simply produce dW/dt=0.
Further, if we attempt to derive a DE for W(t) by simply taking the time derivative of CUBIC’s cwnd, we must still take into account the time dependencies of s(t) and Wmax(t). The result would be a differential equation for W(t) that depends not only on s and Wmax, but also on their derivatives with respect to time. In other words, we need expressions for ds/dt and dWmax/dt. Moreover, note that s and Wmax are variables that all loss-based protocols have in common. Using this to our advantage, we set out to derive a system of differential equations that describe the behavior of the time since last loss and the maximum window size, rather then the congestion window.

## Slide 31: Current and Future Work
Developed a linearizable version of CUBIC.
  Simulations show that while this controller is more responsive, it is also less stable.
Application of fluid model to H-TCP.
  Conditions derived for stability.
  Simulations show that H-TCP in general less stable than CUBIC.

## Slide 32: Examples

## Slide 33: Model Validation
Notes: Possible application of what we’ve learned: more intelligent ssthresh choices.