## Slide 1: Let the Market Drive Deployment A Strategy for Transitioning to BGP Security
Phillipa Gill
University of Toronto
Sharon Goldberg
Boston University
Michael Schapira
Princeton University
SIGCOMM 2011
Toronto, ON
Aug. 16, 2011
Notes: Load = 20 msges per second.

## Slide 2: Incentives for BGP Security
Insecurity of Internet routing is well known:
S-BGP proposed in 1997 to address many issues
Challenges are being surmounted:
  Political: Rollout of RPKI as a cryptographic root trust
  Technical: Lots of activity in the IETF SIDR working group
The pessimistic view:
This is economically infeasible!
Why should ISPs bother deploying S*BGP?
No security benefits until many other ASes deploy!
Worse yet, they can’t make money from it!
Our view:
Calm down. Things aren’t so bad.
ISPs can use S*BGP to make money
…by attracting traffic to their network.

## Slide 3: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 4: Traffic Attraction & Interception Attacks
ChinaTel path is shorter
?
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel 66.174.161.0/24
Level3, VZW, 22394 66.174.161.0/24
22394
  This prefix and 50K others were announced by China Telecom
  Traffic for some prefixes was possibly intercepted
  April 2010 : China Telecom intercepts traffic
66.174.161.0/24
VZW, 22394 66.174.161.0/24
22394 66.174.161.0/24

## Slide 5: Securing the Internet: RPKI
  Resource Public Key Infrastructure (RPKI): Certified mapping from ASes to public keys and IP prefixes.
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel 66.174.161.0/24
?
Level3, VZW, 22394 66.174.161.0/24
22394
X
RPKI: Invalid!
  RPKI shows China Telecom is not a valid origin for this prefix.

## Slide 6: But RPKI alone is not enough!
  Resource Public Key Infrastructure (RPKI): Certified mapping from ASes to public keys and IP prefixes.
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel, 22394 66.174.161.0/24
?
Level3, VZW, 22394 66.174.161.0/24
22394
  Malicious router can pretend to connect to the valid origin.

## Slide 7: To stop this attack, we need S*BGP (e.g. S-BGP/soBGP) (1)
China
Telecom
ISP 1
Verizon
Wireless
Level 3
22394
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
VZW: (22394, Prefix)
Public Key Signature: Anyone with 22394’s public key can validate that the message was sent by 22394.
  S-BGP [1997]: RPKI + Cannot announce a path that was not announced to you.
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
ISP 1: (Level3, VZW, 22394, Prefix)

## Slide 8: To stop this attack, we need S*BGP (e.g. S-BGP/soBGP) (2)
China
Telecom
ISP 1
Verizon
Wireless
Level 3
22394
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
ISP 1: (Level3, VZW, 22394, Prefix)
  Malicious router can’t announce a direct path to 22394, since 22394 never said
ChinaTel: (22394, Prefix)
  S-BGP [1997]: RPKI + Cannot announce a path that was not announced to you.

## Slide 9: Overview
S*BGP will necessarily go through a transition phase
How should deployment occur?
Our Goal: Come up with a strategy for S*BGP (S-BGP/soBGP) deployment.
How governments & standards groups invest resources
… to create market pressure for S*BGP deployment
We evaluate guidelines via a model & simulations
Model: ISPs care only about revenue, not security!
And run simulations on [UCLA Cyclops+IXP] AS graph data
Parallelize simulations on a 200-node DryadLINQ cluster

## Slide 10: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 11: How to deploy S*BGP globally?
Pessimistic view:
No local economic incentives; only security incentives
Like IPv6, but worse, because entire path must be secure
Our view:
S*BGP has an advantage: it affects route selection
Route selection controls traffic flows
And an ISP that attracts more customer traffic earns more revenue.
8359
Why should I upgrade if (security) benefits don’t kick in unless everyone else does?

## Slide 12: Stubs vs ISPs: Stubs are 85% of the Internet’s ASes!
  A stub is an AS with no customers.
  Stubs shouldn’t transit traffic. They only originate their own prefixes.
8359
Sprint
18608
13789
  ISP
  ISP
  ISP
$
$
  Stub
  85% of ASes are stubs! We call the rest (15%) ISPs.
Loses $$!
X

## Slide 13: How can we create market pressure?
  ISP
  ISP
  ISP
  Stub
8359
Sprint
18608
13789
18608
38.101.185.0/24
8359, 18608
38.101.185.0/24
18608
38.101.185.0/24
13789, 18608
38.101.185.0/24
ISPs can use S*BGP to attract customer traffic & thus money
$
$
  Assume that secure ASes break ties on secure paths!
  AS 8359 attracts customer traffic

## Slide 14: How can we create market pressure?
  Assume that secure ASes break ties on secure paths!
  AS 8359 loses traffic, feels pressure to deploy.
8359
Sprint
18608
18608
38.101.185.0/24
8359, 18608
38.101.185.0/24
13789
$
$
13789: (18608, 38.101.185.0/24)
13789: (18608, 38.101.185.0/24)
Sprint: (13789, 18608, 38.101.185.0/24)

## Slide 15: Our Strategy: 3 Guidelines for Deploying S*BGP (1)
Secure ASes should break ties in favor of secure paths
ISPs “help” their stub customers deploy simplex S*BGP.
ISP1
Boston U
Bank of A
A stub is an AS that does not transit traffic.
85% of ASes are stubs!
Boston U
Bank of A

## Slide 16: Simplex S*BGP: `Cheap’ S*BGP for Stubs
A stub never transits traffic
Only announces its own prefixes..
…and receives paths from provider
Sign but don’t verify!
(rely on provider to validate)
2 options for deploying S*BGP in stubs:
Have providers sign for stub customers. (Stubs do nothing)
Stubs run simplex S*BGP. (Stub only signs, provider validates)
  No hardware upgrade required
    Sign for ~1 prefix, not ~300K prefixes
    Use ~1 private key, not ~36K public keys
  Security impact is minor (we evaluated this):
    Stub vulnerable to attacks by its direct provider.
18608
  Stub
18608
38.101.185.0/24

## Slide 17: Our Strategy: 3 Guidelines for Deploying S*BGP (2)
Secure ASes should break ties in favor of secure paths
ISPs “help” their stub customers deploy simplex S*BGP.
(possibly with some government subsidies)
3. Initially, a few early adopters deploy S*BGP (gov’t incentives, regulations, altruism, etc).
ISP1
Boston U
Bank of A

## Slide 18: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 19: A model of the S*BGP deployment process
To start the process:
  Early adopter ASes have deployed S*BGP
  Their stub customers deploy simplex S*BGP
Each round:
  Compute utility for every insecure ISP
  If its ’ ‘s utility can increase by more than θ%
  when it deploys S*BGP,
  Then SP n decides to secure itself & all its stub customers
Stop when no new ISPs decide to become secure.
ISP n
ISP n
ISP n

## Slide 20: How do we compute utility?
    Number of source ASes
routing through ISP n
to all customer destinations.
ISP n
$
$
$
ISP n
BGP Routing Policy Model:
1. Prefer customer paths
over peer paths
over provider paths
2. Prefer shorter paths
3. If secure, prefer secure paths
.
4. Arbitrary tiebreak
To determine routing,
we run simulations on the
[UCLA Cyclops] AS graph
with these routing policies:
Important Note: ISP utility does not depend on security.
traffic

## Slide 21: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 22: Case Study of S*BGP deployment
Ten early adopters:
Five Tier 1s:
  Sprint (AS 1239)
  Verizon (AS 701)
  AT&T (AS 7018)
  Level 3 (AS 3356)
  Cogent (AS 174)
The five content providers source 10% of Internet traffic
Stubs break ties in favor of secure paths
Threshold θ = 5%.
Five Popular Content Providers
  Google (AS 15169)
  Microsoft (AS 8075)
  Facebook (AS 32934)
  Akamai (AS 22822)
  Limelight (AS 20940)
This leads to 85% of ASes deploying S*BGP
(65% of ISPs)

## Slide 23: Simulation: Market pressure drives deployment (1)
Round 0
13789
Sprint
8359
18608
13789
18608
8359
Round 1
Round 4
  Stub

## Slide 24: Simulation: Market pressure drives deployment (2)
Round 4
Sprint
8359
8342
30733
6731
50197
13789
18608
6731
50197
Round 5
  Stub
  Stub

## Slide 25: Simulation: Market pressure drives deployment (3)
Sprint
8359
8342
30733
6731
50197
13789
18608
6731
50197
8342
41209
9002
43975
39575
Round 6
41209
39575
Round 7
  Stub
  Stub
  Stub

## Slide 26: So who should be the early adopters?
Theorem: Finding the optimal set of early adopters is NP-hard. Approximating this within a constant factor is also NP-hard.

## Slide 27: So who should be the early adopters?
Small target set suffices for small threshold
Higher threshold
requires a larger target set.
Easy to deploy
Hard to deploy

## Slide 28: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 29: Summary and Recommendations
  How to create a market for S*BGP deployment?
  Many secure destinations via simplex S*BGP.
  Market pressure via S*BGP influence on route selection.
  Where should government incentives and regulation go?
  Focus on early adopters; Tier 1s, maybe content providers
  Subsidize ISPs to upgrade stubs to simplex S*BGP
  Other challenges and future work :
  ISPs can have incentives to turn off S*BGP
  BGP and S*BGP will coexist in the long run
  ISPs need tools to predict S*BGP impact on traffic

## Slide 30
  Contact: phillipa@cs.toronto.edu
  http://www.cs.toronto.edu/~phillipa/sbgpTrans.html
  Thanks to Microsoft Research SVC and New England for supporting us with DryadLINQ.

## Slide 31: Data Sources for ChinaTel Incident of April 2010
Example topology derived from Routeviews messages observed at the LINX Routeviews monitor on April 8 2010
  BGP announcements & topology was simplified to remove prepending
  We anonymized the large ISP in the Figure.
  Actual announcements at the large ISP were:
  From faulty ChinaTel router: “4134 23724 23724 for 66.174.161.0/24”
  From Level 3: “3356 6167 22394 22394 for 66.174.161.0/24”
Traffic interception was observed by Renesys blog
  http://www.renesys.com/blog/2010/11/chinas-18-minute-mystery.shtml
  We don’t have data on the exact prefixes for which this happened.
AS relationships: inferred by UCLA Cyclops